## Slide 1: Kinetics of Dye Regeneration in Photoanodes of Dye-Sensitized Solar Cells
Institute of Chemistry, Carl von Ossietzky University of Oldenburg, D-26111, Germany contact: wasiu.hamzat@uol.de; Cooperating partner: Institute of Applied Physics, Justus-Liebig University of Giessen.
[1] R. Ruess, S. Scarabino, A. Ringleb, K. Nonomura, N. Vlachopoulos, A. Hagfeldt, G. Wittstock, D. Schlettwein; Phys. Chem. Chem. Phys. 2019, 21, 13047-13057 [2] S. Scarabino, PhD Thesis, University of Oldenburg, 2020 {3] S. Scarabino, K. Nonomura, N. Vlachopoulos, A. Hagfeldt, G. Wittstock; Electrochem 2020, 1, 329-343 [4] H. Ellis, I Schmidt, A. Hagfeldt, G. Wittstock, G. Boschloo; J. Phys. Chem. C 2015, 119, 21775–21783.
Wasiu Abidemi Hamzat, Gunther Wittstock, Dmitry Momontenko,Marius Muhle
The simulation describe diagnostic experiments of photoanodes with scanning electrochemical microscopy (SECM) with the aim of extracting the maximum information content from experiment.
An approach curve obtained by scanning electrochemical microscopy (SECM) represents the electrolysis current for a mediator at microelectrode as function of sample-microelectrode distance. It contains information about the reaction rate by which the mediator is regenerated at the sample -- here the illuminated photoanode from a dye-sensitized solar cell. Quantitative relations are available for flat electrodes, the overlapping effects of electrode porosity, decaying light intensity on the sample, loss mechanisms in the porous semiconductor on the microelectrode current have not been understood quantitatively. The simulation are made to understand the steady state behavior and also the time-dependent behavior for intermittent illumination which is expected to contain more kinetic information of the studied system. Our simulation describes the process of light absorption, electron injection into the conduction band, dye regeneration by the mediator, loss processes.
Introduction
Computational Method
Figure 1: Simulation model and geometry.
Simulation results
Figure 3: Concentration of profile of mediator and calculated conduction band electrons along a symmetry axis.
Figure 2: Approach curves with increasing intensity of light of photoanode and its comparison with experiment at 1.8 µm
[Dye] > >
(From experiment)
[Dye+]
Lambert-Beer Law
Diffusive mass transport for MRed, MOx, eCB
Physic 1
Diffusion of dilution species (MRed, MOx)
Boundary conditions
Bulk boundaries: 10, 11
DMOx= DMRed= De-= 9.1E-10 m²/s,
cMox=1 mM, cRed=0, rT=25 µM
5,3,1,13,12, no flux
Porous domain
Porosity (por) = 0.6, α = 0.2µm,
Keq=50m2s/mol, Dpor=D[MOx]por1.5
Reactions in the porous domain
RMox =kox[Dye+][Mred], RMRed =kox[Dye+][Mred], kox= 10 m3/(smol), Ddye=1E-20 m/s,
Physics 2: (eCB)
Boundary conditions
At z=-d_film
(back contact) [ecB]=0,
At symmetry
At tip, JMox=kT[MOx], RMRed =- kox[MOx], kT= 1 m/s
Generation of eCB
ReCB= α Jhve- α z
Initial condition: [ecB]=0
To be done
consumption terms (loss mechanisms)
Dye regeneration by mediator
Electron injection, photoxidation of dye
Microelectrode current