## Slide 1
Multiphysics field topology optimization design of heat conduction structure of high-temperature superconducting magnets
Shao Qing1, Li Kai1, Shao Nan1, Wu Wei2,3, Yu Qingsong1, Liang Shikuan1, Tan Fuxing1, Hu Hao1, Wang Aibin1, Liu Hongtao1, Wu Chen1, Wang Yunxiao1, Gao Chunyao1
Maglev technology institute, CRRC Changchun Railway Vehicles Co., Ltd.
Shanghai Jiaotong University
Shanghai Superconducting Technology Co., Ltd.
Notes: 各位同仁，大家上午好。我来自中车长春轨道客车股份有限公司，我的主题是高温超导磁体的热传导结构的多物理场拓扑优化，很高兴能有机会和大家分享我们的基于COMSOL软件的一些研究成果，下面是我们的团队成员。

## Slide 2: Outline
Background
Problem Description
Topology Optimization
Results & Comparisons
Conclusions
FRI-OR6-701-04
Notes: 我的分享分为5个部分

## Slide 3: Background
Motivations
Japan， Yamanashi test line: L0
2015.04, 603 km/h, Word Record
Superconducting electrodynamic suspension
[4] K. Mizuno et al. SUST 2020,33, 074009
[2] K. Mizuno et al, IEEE TASC, 2017, 27(4) 3600205
[3] K. Mizuno et al, IEEE TASC, 2018, 28(4) 3601107
The superconducting magnet based on the second-generation HTS ReBCO
The superconducting magnet based on the first-generation high-temperature superconducting ( HTS )
[1] M. Terai et al, IEEE TASC, 2006, 1124-1129
BSCCO
Notes: 首先，我想介绍一下研究动机和研究背景。
由于轨道交通领域对更高速度的追求，在世界范围内广泛地开始了占领高速磁浮技术高地的竞争，日本于1962年开始超导磁浮技术的研究，2015年实现603km/h的载人试验，暂未实现工程化应用
美国也于20世纪60年代开始磁浮技术研究，2020年首次完成载人测试，试验速度172km/h，同样暂未实现工程化应用。
国内，中车长客和航天三院等单位针对超导电动悬浮关键技术和工程化研究也开展了深入的研究，形成了比较完善的技术体系。
目前低温超导磁悬浮列车的世界速度纪录为603公里/小时，由日本JR Central在其山梨试验线上创造。
然而，与在4.2 K以下工作的低温超导磁体相比，基于第二代高温超导带的超导磁体可以在15 K至77 K下工作。
高温超导磁体的制冷成本较低，可以摆脱中国稀缺的液氦资源。

## Slide 4: Background
Challenges in Specific Applications
Develop 4 on-board ReBCO magnets for a prototype maglev train
Built by CRRC Changchun Railway Vehicles
In very limited vehicle space: 4×1.6m
In very limited vehicle weight: <2.5 t
Limited pole size: 464×324×66 mm
Limited magnetomotive force: ~360 kA
Weight of a single superconducting magnet: <500 kg
Rated Functioning Temperature: <35 K
No power supply on the vehicle
operated in “power-off” mode
Persistent current mode independent operation of left and right poles
(<1.1%/day )
Strictly controlled volume, weight and budget
Notes: 为了进一步验证基于高温超导磁体的超导电动悬浮磁悬浮列车的可行性，我公司建立了一条200米的高温超导全要素试验系统。
下图显示了试车线的原型、轨道和设计指标。

## Slide 5: Background
Electromagnetic, Thermal and Mechanical Coupled Design
Rated Functioning Temperature: <35 K
Total heat leakage as low as possible
Offline running time: > 1 h
Cooperate with stator coil to ensure Traction force design target
Cooperate with 8 coil to ensure Levitation force design target
(I/Ic) < 60% @35 K
Thermal Design
Electromagnetic Design
Mechanical
Design
Levitation force
Guidance force
Traction force
Lorentz force
Maximum von-Mises stress: < 25% allowable stress
Weight <500 kg
Electromagnetic loss
Lightweight magnet support structure
Strong enough mechanical properties
Acceptable conduction heat load
Challenges in Specific Applications
Thermal stress
Notes: 作为系统中最核心的部分，高温超导磁体是全要素试验系统设计中最困难的部分之一。
其设计需要综合应用电磁、温度、力学等领域的关键技术。
从图中可以看出，每个物理场都有相应的设计目标，不同物理场之间有很多耦合因素。
作为磁体结构的主要承载部分，本研究进一步优化了主支撑。

## Slide 6: Background
Topology optimization
Homogenization (1988)
SIMP/RAMP (1989)
ESO/BESO (1992)
Independent continuous mapping (1996)
Level-set (2002)
Notes: 其次，让我们重点介绍结构优化方法。
一般来说，优化方法可分为左图中的三类。
其中，拓扑优化方法比其他两种优化方法具有更大的设计自由度。
基于变密度方法的拓扑优化方法，如1989年提出的SIMP算法，已被广泛应用于工程实践。此外，它可以为多物理场耦合情况下的结构轻量化设计提供概念指导，而不依赖于设计师的经验。

## Slide 7: Background
Topology optimization
Notes: 以下是拓扑优化在空客A380翼盒肋结构和汽车轮毂减重应用中的应用，以及散热结构和流道优化应用。
在这项研究中，拓扑优化被扩展到多物理场耦合应用。

## Slide 8: Problem Description
COMSOL Physics Implementation
Governing Equations
Electromagnetic, Thermal and Mechanical Coupled Design
Temperature Field
Electromagnetic Field
Structure Field
H is the magnetic field intensity,J is the current density,D is the electric displacement,E is the electric field intensity,B is magnetic induction intensity,ρ is the bulk charge density,μ is the permeability,Sigma is electrical conductivity,ε is the dielectric constant
ρ is the material density;C is specific heat of material;a is thermal diffusivity,a= λ /(c ρ);T is time; λX,λy, λz is the thermal conductivity coefficient of the material along the x, y and z directions;Vq is the heat flux emitted per unit volume and per unit time
u, ε, σ are displacement, strain, stress respectively.F power vector, D is the elastic matrix, depends on the elastic modulus of the elastic material E and Poisson's ratio ν; ρ is mass density, μ is damping coefficient
Sequential coupling
Direct coupling
Notes: 为了解决多目标多场耦合拓扑优化问题，我们首先需要明确每个物理场之间的耦合策略。
在这项研究中，电磁场和结构场之间采用了顺序耦合方法，并通过解析方法将电磁力作为结构场中的边界条件求解。
温度场和结构场之间采用直接耦合方法，相互考虑两个场之间的相互作用。
电磁场和温度场之间的电磁损失对主支架的设计影响很小，因此本次不考虑其影响。

## Slide 9: Problem Description
COMSOL Physics Implementation
Lightweight magnet support structure
Strong enough mechanical properties
Ensure the levitation and guidance force meet the design target
Acceptable conduction heat load
Keep the weight as low as possible
Notes: 根据主支撑位置和线圈支撑位置，将待优化的主支撑结构（即设计区域）简化为右图所示的形式。该优化设计要达到的设计目标如下。

## Slide 10: Topology Optimization
Theory of Topology Optimization
Design domain is discretized
Each element is assigned a design variable
In practice, we define an artificial density function , which is between 0 and 1 for each point of the geometry.
For a structural mechanics simulation, this function is used to build a penalized Young’s modulus:
For a temperature simulation, this function is used to build a penalized coefficient of heat conductivity k and heat capacity C:
where E0 ,k0, C0 are the true Young’s modulus, coefficient of heat conductivity and heat capacity, respectively. Thus, ρdesign= 0 corresponds to a void part and ρdesign = 1 corresponds to a solid part.
Notes: 此外，主支撑结构的设计区域被离散化。每个元素都被分配了一个设计变量。
在基于变量密度法的拓扑优化中，设计变量是每个元素的相对密度，通过改变每个元素的相关密度值来实现结构的优化设计
在结构领域，杨氏模量用于构建元素的相对密度。
在温度场中，元素的相对密度由材料的导热系数和比热构成。

## Slide 11: Topology Optimization
Implementation of Topology Optimization
Boundary conditions
Optimization
Structure Field
Levitation force: 2500 N
Guidance force: 2000 N
Traction force: 5000 N
Lorentz force: 8000 N
Gravity
Temperature Field
293 K-20 K
Material: TC4 + 6061-T6
Notes: 电磁力作为结构场中的边界条件，通过解析方法求解。
在此基础上，考虑重力效应和主支架冷热端温差，进行了热力耦合分析。
为了实现主支架的高负载和低热泄漏的设计目标。拓扑优化的目标是使总应变最小化
设计区域同时存在能量和热量泄漏。
约束条件是设计区域内材料的最大应力不超过材料屈服极限的85%，体积分数约束条件不超过设定值。

## Slide 12: Topology Optimization
Implementation of Topology Optimization
Step 10
Step 30
Step 50
Step 70
Notes: 下图显示了在拓扑优化迭代的第10步、第30步、第50步和第70步中，在设计区域中逐步计算对优化目标贡献最大的材料分布的情况。

## Slide 13: Topology Optimization
Implementation of Topology Optimization
10%
20%
30%
40%
Volume fraction
Notes: 下图显示了当体积分数设置为10%、20%、30%和40%时的相应拓扑优化结构。体积分数越大，设计区域中保留的材料越多。

## Slide 14: Topology Optimization
Implementation of Topology Optimization
Smooth design
Notes: 然后，选择体积分数为20%的拓扑优化结果进行平滑处理，以获得如下图所示的最终结构。

## Slide 15: Results & Comparisons
Implementation of Topology Optimization
Compared with the model before optimization
85% weight reduction
Maximum von-Mises stress increased by 15% （< 25% allowable stress ）
Heat leakage decreased by 61.7%
Notes: 与原始结构相比，优化结果可以减轻85%的重量，减少61.7%的热泄漏。尽管最大Von mises应力增加了15%，但它仍然达到了低于材料屈服极限85%的设计目标。结果表明，多物理场拓扑优化方法采用了一种新型的结构，实现了主支架高负载、低热泄漏的设计目标。

## Slide 16: Conclusions
Conclusion
Implemented direct coupling between structure field and temperature field
Implemented sequential coupling between structure field and electromagnetic field
Implemented topology optimization of electromagnetic and thermal multi-physical field and multi-objective
85% weight reduction
Maximum von-Mises stress increased by 15% （< 25% allowable stress ）
Heat leakage decreased by 61.7%
Strong enough mechanical properties
Acceptable conduction heat load
FRI-OR6-701-04
Notes: 通过上述对多目标多物理场耦合拓扑优化的研究，我们可以得出以下结论。
此外，通过拓扑优化获得的结构将通过工程验证，基于这种方法的多物理场耦合可以进一步优化高温超导磁体的其他重要部件。

## Slide 17
Thanks!
Q&A
Notes: 以上是我全部的分享内容，谢谢