## Slide 1
New Insights into Rheological Properties of Drilling Mud at Some Laboratory Testing Temperatures and its Cuttings Carrying Performance via Reelwell Drilling Method
Presented by: Xiao Fei
2024.10.31

## Slide 2
01
OUTLINE
05
04
03
02
01
研究目的
仿真结果
结论
研究方法
背景介绍

## Slide 3
01
背景介绍
Schematic diagram of Reelwell Drilling Method (RDM) (after Hurum 2015)
Schematic diagram of traditional drilling method (Mikhail Gelfgat, 2022)

## Slide 4
01
背景介绍
Reelwell Drilling Method主要优势
提高效率：使用双壁钻杆和特殊的流动转换装置，可实现更高效的岩屑携带和钻井液循环。
减少环境影响：实现闭环循环系统，可减少钻井液使用和排放。
更好的井底压力控制：避免地层损害和提高油气产量
适用于复杂地质条件：适用于水平井或大位移钻井，能够在复杂的地质条件下保持高效的钻井作业。
减少钻杆扭矩和拖拽力：通过特殊的浮力技术，可显著减少钻杆的扭矩和拖拽力，有助于延长钻杆的使用寿命和提高钻井效率。
提高井筒清洁度：更快的岩屑运输速度，从而保持井筒的清洁，对于钻水平井尤为重要。
减少钻井液密度：可在较低的钻井液密度下进行钻井，这有助于减少钻压，避免地层损害，同时提高钻井效率。
提高钻井深度：在开放孔延伸极限的预测模型中显示出与传统钻井方法相比有显著的改进。
实时地层评估：RDM 技术可以在钻井过程中进行实时地层评估，因岩屑高速返回地面，未受机械研磨与混合影响，可减少对岩心取样、井下测井和使用高级测井工具的需求。
Schematic diagram of Reelwell Drilling Method (after Hurum 2015)

## Slide 5
01
背景介绍
Schematic diagram of traditional drilling method (Mikhail Gelfgat, 2022)
较之Reelwell Drilling Method，传统钻井方法的主要不足
钻井速度慢：传统钻井方法需要频繁地将钻杆接长，这不仅耗时而且效率低下。而在RDM中，使用的是连续的管材，可以快速下放和回收，大大提高了钻井速度。
成本较高：传统钻井过程中，由于需要不断添加钻杆，增加了作业时间和人力成本。此外，每次更换钻杆时还需要停机，导致了额外的时间损失。相比之下，RDM减少了这些不必要的操作，降低了整体成本。
环境影响较大：传统钻井方法可能会产生更多的废弃物，如废弃的钻杆等，对环境造成一定负担。而RDM由于其高效性和减少材料使用的特点，有助于减轻对环境的影响。
安全风险：在传统钻井过程中，频繁的操作增加了工人受伤的风险。例如，在连接和拆卸钻杆时可能发生意外。RDM通过减少此类操作，提高了作业的安全性。
灵活性较低：传统钻井设备往往体积庞大，移动不便，难以适应复杂地形条件下的作业需求。而RDM使用的连续管更加轻便灵活，能够更好地应对各种地质条件。
维护成本高：传统钻井设备复杂，维护成本相对较高。RDM则因为系统设计更为简化，维护起来更加方便快捷，从而降低了维护成本。

## Slide 6
01
背景介绍
Reelwell Drilling Method的研究现状：
主要涉及钻井液（Drilling mud）流变特性及其挟岩能力（Cuttings carring capacity）评估
钻井液流变特性：目前两参数（包括Casson model、Power law model、Bingham model等）、三参数（包括Herschel-Bulkley model、Bingham-Papanastasiou model 、Robertson-Stiff model等）的流变模型很多，缺乏表征温度影响的高精度连续模型。
钻井液挟岩能力：传统钻井方法相关研究较多，包括倾斜钻井内岩屑的沉积、岩屑对于管壁的侵蚀、倾斜角及温度的影响等，实验研究多采用接近实际的钻井液与岩屑，但成本通常较高（全尺寸现场试验更是贵得离谱）；数值仿真性价比高，但目前多采用两相流或稀释物质的输送模型来计算，与实际情况相差甚远。
新模型开发需求：亟需开发符合钻井液流变特性及岩屑运移特征的模型。
Rock cuttings are carried out by drilling mud (active mud) via the inner tube of a dual-wall drill pipe
(Figure source: https://www.reelwell.com/dualpipe)

## Slide 7
02
研究目的
油气/地热能开采成本高企，需降本增效，RDM成为首选
自主研发
国内大型油气公司大概率被限购或价格高企，迫切需要自主研发相关设备
购买途径
Reelwell 公司正在准备将这项技术商业化，目前商业市场上尚无购买信息
现实需求
有
无
须
Figure source：https://www.lrpartners.com/portfolio/reelwell/

## Slide 8
03
研究方法
Reelwell Drilling Method (RDM) : demonstration video
钻井液挟岩能力评估技术路线

## Slide 9
04
仿真结果
钻井液流变特性测试实验
测试温度 (℃)：4、10、16、22、28、34、40、46、52、58、64、70
测试剪切率 (1/s)：3.178、4.313、5.675、7.378、10.22、15.89、21.57、28.38、36.89、51.08、63.56、86.28、113.5、147.6、201.4
Some devices used for laboratory (a) XYM-3 densitometer and (b) thermostatic bath system and NXS-11B rotary viscometer (right)
(a)
(b)

## Slide 10
04
仿真结果
钻井液流变特性测试数据
Table 1 Laboratory testing of shear stress-shear rate and the associated fitting coefficients of the Bingham model
(1/s) | 3.178 | 4.313 | 5.675 | 7.378 | 10.22 | 15.89 | 21.57 | 28.38 | 36.89 | 51.08 | 63.56 | 86.28 | 113.5 | 147.6 | 201.4
τ (Pa) | 3.52 | 3.75 | 4.20 | 4.65 | 5.22 | 6.24 | 7.26 | 8.51 | 9.76 | 11.80 | 13.39 | 16.46 | 19.41 | 22.93 | 28.38
T=4℃ | R2 = 0.9866, =4.265 (3.566,4.964) *, =0.1274 (0.1185,0.1363) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 3.18 | 3.29 | 3.52 | 3.97 | 4.43 | 5.33 | 6.24 | 7.26 | 8.51 | 10.22 | 11.80 | 14.30 | 17.59 | 20.43 | 25.65
T=10℃ | R2 = 0.9899, =3.564 (3.013, 4.114), =0.1158 (0.1088, 0.1228) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.95 | 3.29 | 3.52 | 3.75 | 4.43 | 4.88 | 5.56 | 6.36 | 7.38 | 9.08 | 10.78 | 12.83 | 14.76 | 18.61 | 23.84
T=16℃ | R2 = 0.9954, =3.251 (2.915, 3.586), =0.1045 (0.1002, 0.1087) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.84 | 3.06 | 3.41 | 3.75 | 3.97 | 4.65 | 5.11 | 5.68 | 6.81 | 8.17 | 9.87 | 11.46 | 13.62 | 16.57 | 21.00
T=22℃ | R2 = 0.9947, =3.132 (2.818, 3.447), =0.09158 (0.08757, 0.09559) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.72 | 2.84 | 2.95 | 3.18 | 3.86 | 4.43 | 5.11 | 5.68 | 6.70 | 7.95 | 9.08 | 10.78 | 12.94 | 15.44 | 19.52
T=28℃ | R2 = 0.9919, =3.016 (2.652, 3.379), =0.08523 (0.0806, 0.08986) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.72 | 2.84 | 2.95 | 3.06 | 3.75 | 4.09 | 4.65 | 5.33 | 5.68 | 7.26 | 8.17 | 9.65 | 11.35 | 13.62 | 17.25
T=34℃ | R2 = 0.9931, =2.92 (2.633, 3.208), =0.0735 (0.06983, 0.07716) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.61 | 2.72 | 2.84 | 3.06 | 3.41 | 3.86 | 4.31 | 4.77 | 5.45 | 6.58 | 7.38 | 8.63 | 10.33 | 12.26 | 15.66
T=40℃ | R2 = 0.995, =2.776 (2.558, 2.993), =0.06554 (0.06277, 0.06831) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.61 | 2.72 | 2.72 | 2.84 | 2.95 | 3.75 | 4.09 | 4.54 | 5.11 | 6.13 | 6.92 | 8.40 | 9.87 | 11.58 | 14.76
T=46℃ | R2 = 0.9947, =2.641 (2.429, 2.853), =0.06195 (0.05925, 0.06465) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.72 | 2.72 | 2.84 | 2.95 | 3.29 | 3.63 | 3.97 | 4.43 | 4.99 | 5.68 | 6.24 | 7.49 | 8.97 | 10.78 | 13.73
T=52℃ | R2 = 0.9983, =2.695 (2.587, 2.803), =0.05524 (0.05387, 0.05662) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.50 | 2.61 | 2.61 | 2.84 | 3.18 | 3.63 | 3.97 | 4.20 | 4.65 | 5.45 | 6.13 | 7.26 | 8.63 | 10.44 | 12.94
T=58℃ | R2 = 0.9964, =2.606 (2.458, 2.754), =0.05265 (0.05076, 0.05453) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.50 | 2.61 | 2.72 | 2.84 | 3.06 | 3.52 | 3.86 | 4.09 | 4.43 | 5.11 | 5.79 | 6.81 | 8.17 | 9.42 | 11.69
T=64℃ | R2 = 0.9952, =2.643 (2.491, 2.794), =0.0464 (0.04446, 0.04833) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.38 | 2.50 | 2.61 | 2.84 | 3.18 | 3.41 | 3.75 | 3.97 | 4.43 | 4.99 | 5.56 | 6.58 | 7.83 | 8.97 | 10.90
T=70℃ | R2 = 0.9912, =2.64 (2.449, 2.831), =0.04303 (0.04059, 0.04547) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 3.178 | 4.313 | 5.675 | 7.378 | 10.22 | 15.89 | 21.57 | 28.38 | 36.89 | 51.08 | 63.56 | 86.28 | 113.5 | 147.6 | 201.4
τ (Pa) | 3.52 | 3.75 | 4.20 | 4.65 | 5.22 | 6.24 | 7.26 | 8.51 | 9.76 | 11.80 | 13.39 | 16.46 | 19.41 | 22.93 | 28.38
T=4℃ |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 3.18 | 3.29 | 3.52 | 3.97 | 4.43 | 5.33 | 6.24 | 7.26 | 8.51 | 10.22 | 11.80 | 14.30 | 17.59 | 20.43 | 25.65
T=10℃ |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.95 | 3.29 | 3.52 | 3.75 | 4.43 | 4.88 | 5.56 | 6.36 | 7.38 | 9.08 | 10.78 | 12.83 | 14.76 | 18.61 | 23.84
T=16℃ |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.84 | 3.06 | 3.41 | 3.75 | 3.97 | 4.65 | 5.11 | 5.68 | 6.81 | 8.17 | 9.87 | 11.46 | 13.62 | 16.57 | 21.00
T=22℃ |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.72 | 2.84 | 2.95 | 3.18 | 3.86 | 4.43 | 5.11 | 5.68 | 6.70 | 7.95 | 9.08 | 10.78 | 12.94 | 15.44 | 19.52
T=28℃ |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.72 | 2.84 | 2.95 | 3.06 | 3.75 | 4.09 | 4.65 | 5.33 | 5.68 | 7.26 | 8.17 | 9.65 | 11.35 | 13.62 | 17.25
T=34℃ |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.61 | 2.72 | 2.84 | 3.06 | 3.41 | 3.86 | 4.31 | 4.77 | 5.45 | 6.58 | 7.38 | 8.63 | 10.33 | 12.26 | 15.66
T=40℃ |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.61 | 2.72 | 2.72 | 2.84 | 2.95 | 3.75 | 4.09 | 4.54 | 5.11 | 6.13 | 6.92 | 8.40 | 9.87 | 11.58 | 14.76
T=46℃ |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.72 | 2.72 | 2.84 | 2.95 | 3.29 | 3.63 | 3.97 | 4.43 | 4.99 | 5.68 | 6.24 | 7.49 | 8.97 | 10.78 | 13.73
T=52℃ |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.50 | 2.61 | 2.61 | 2.84 | 3.18 | 3.63 | 3.97 | 4.20 | 4.65 | 5.45 | 6.13 | 7.26 | 8.63 | 10.44 | 12.94
T=58℃ |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.50 | 2.61 | 2.72 | 2.84 | 3.06 | 3.52 | 3.86 | 4.09 | 4.43 | 5.11 | 5.79 | 6.81 | 8.17 | 9.42 | 11.69
T=64℃ |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
τ (Pa) | 2.38 | 2.50 | 2.61 | 2.84 | 3.18 | 3.41 | 3.75 | 3.97 | 4.43 | 4.99 | 5.56 | 6.58 | 7.83 | 8.97 | 10.90
T=70℃ |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Note*: The numbers in parentheses represent the 95% confidence bounds.

## Slide 11
02
仿真结果
钻井液流变特性测试数据
Table 2 Laboratory testing of apparent viscosity-shear rate and the associated fitting coefficients of the Bingham-Papanastasiou model
(1/s) | 3.178 | 5.675 | 10.22 | 21.57 | 113.5 | 147.6 | 201.4
(mPa·s) | 1107.32 | 740.00 | 511.15 | 336.90 | 171.00 | 155.37 | 138.90
T=4℃ | R2= 0.9974, =3.714 (3.114, 4.314), 0.1371 (0.1004, 0.1738), =0.5493 (0.3063, 0.7923) |  |  |  |  |  | 
(mPa·s) | 1000.16 | 620.00 | 433.37 | 289.52 | 155.00 | 138.46 | 125.56
T=10℃ | R2= 0.9971, =2.917 (2.472, 3.363), 0.1286 (0.09514, 0.1621), =0.9258 (0.06946, 1.782) |  |  |  |  |  | 
(mPa·s) | 928.72 | 620 | 433.37 | 257.93 | 136 | 126.14 | 116.68
T=16℃ | R2= 0.9987, =3.153 (2.789, 3.517), 0.1076 (0.08538, 0.1298), =0.5455 (0.3743, 0.7167) |  |  |  |  |  | 
(mPa·s) | 893 | 600 | 388.92 | 236.88 | 120 | 112.31 | 102.79
T=22℃ | R2= 0.9999, =3.013 (2.908, 3.118), 0.09243 (0.0858, 0.09906), =0.5836 (0.5238, 0.6433) |  |  |  |  |  | 
(mPa·s) | 851.28 | 520.00 | 377.81 | 236.88 | 114.00 | 104.61 | 95.56
T=28℃ | R2= 0.9951, =2.582 (2.061, 3.103), 0.09605 (0.05839, 0.1337), =0.8168 (0.03164, 1.602) |  |  |  |  |  | 
(mPa·s) | 857.28 | 520.00 | 366.70 | 215.82 | 100.00 | 92.30 | 84.45
T=34℃ | R2= 0.9969, =2.642 (2.217, 3.067), 0.08087 (0.04983, 0.1119), =0.8407 (0.1615, 1.52) |  |  |  |  |  | 
(mPa·s) | 821.56 | 500.00 | 333.36 | 200.03 | 91.00 | 83.07 | 76.67
T=40℃ | R2= 0.9986, =2.524 (2.261, 2.788), 0.07125 (0.05159, 0.09092), =0.9007 (0.362, 1.439) |  |  |  |  |  | 
(mPa·s) | 821.56 | 480.00 | 288.91 | 189.50 | 87.00 | 78.46 | 72.23
T=46℃ | R2= 0.9992, =2.395 (2.22, 2.569), 0.06396 (0.05286, 0.07506), =6.484 (-1.548e7, 1.548e7) |  |  |  |  |  | 
(mPa·s) | 857.28 | 500.00 | 322.25 | 184.24 | 79.00 | 73.07 | 67.23
T=52℃ | R2= 0.9993, =2.552 (2.381, 2.724), 0.05929 (0.04509, 0.07349), =1.579 (-1.528, 4.687) |  |  |  |  |  | 
(mPa·s) | 785.84 | 460.00 | 311.14 | 184.24 | 76.00 | 70.77 | 63.34
T=58℃ | R2= 0.9977, =2.359 (2.054, 2.664), 0.06041 (0.03615, 0.08466), =1.175 (-0.4622, 2.813) |  |  |  |  |  | 
(mPa·s) | 785.84 | 480.00 | 300.02 | 178.98 | 72.00 | 63.84 | 57.23
T=64℃ | R2= 0.9993, =2.495 (2.303, 2.687), 0.05087 (0.03676, 0.06498), =0.8604 (0.5137, 1.207) |  |  |  |  |  | 
(mPa·s) | 750.12 | 460.00 | 311.14 | 173.71 | 69.00 | 60.76 | 53.34
T=70℃ | R2= 0.9974, =2.485 (2.107, 2.864), 0.04867 (0.02278, 0.07456), =0.7032 (0.3024, 1.104) |  |  |  |  |  | 
 | 3.178 | 5.675 | 10.22 | 21.57 | 113.5 | 147.6 | 201.4
(mPa·s) | 1107.32 | 740.00 | 511.15 | 336.90 | 171.00 | 155.37 | 138.90
T=4℃ |  |  |  |  |  |  | 
(mPa·s) | 1000.16 | 620.00 | 433.37 | 289.52 | 155.00 | 138.46 | 125.56
T=10℃ |  |  |  |  |  |  | 
(mPa·s) | 928.72 | 620 | 433.37 | 257.93 | 136 | 126.14 | 116.68
T=16℃ |  |  |  |  |  |  | 
(mPa·s) | 893 | 600 | 388.92 | 236.88 | 120 | 112.31 | 102.79
T=22℃ |  |  |  |  |  |  | 
(mPa·s) | 851.28 | 520.00 | 377.81 | 236.88 | 114.00 | 104.61 | 95.56
T=28℃ |  |  |  |  |  |  | 
(mPa·s) | 857.28 | 520.00 | 366.70 | 215.82 | 100.00 | 92.30 | 84.45
T=34℃ |  |  |  |  |  |  | 
(mPa·s) | 821.56 | 500.00 | 333.36 | 200.03 | 91.00 | 83.07 | 76.67
T=40℃ |  |  |  |  |  |  | 
(mPa·s) | 821.56 | 480.00 | 288.91 | 189.50 | 87.00 | 78.46 | 72.23
T=46℃ |  |  |  |  |  |  | 
(mPa·s) | 857.28 | 500.00 | 322.25 | 184.24 | 79.00 | 73.07 | 67.23
T=52℃ |  |  |  |  |  |  | 
(mPa·s) | 785.84 | 460.00 | 311.14 | 184.24 | 76.00 | 70.77 | 63.34
T=58℃ |  |  |  |  |  |  | 
(mPa·s) | 785.84 | 480.00 | 300.02 | 178.98 | 72.00 | 63.84 | 57.23
T=64℃ |  |  |  |  |  |  | 
(mPa·s) | 750.12 | 460.00 | 311.14 | 173.71 | 69.00 | 60.76 | 53.34
T=70℃ |  |  |  |  |  |  | 
Notes: Due to equipment limitations, only the apparent viscosity under low and high shear rate were measured

## Slide 12
02
仿真结果
钻井液流变特性曲面构建：
基于二次拟合，Bingham Surface Model
Fitting of (a) plastic viscosity (R2=0.9939) and (b) yield stress (R2=0.9911) as a function of temperature with data from Table 1 for the Bingham model; (c) building of rheological surface models based on the Bingham models in comparison with the testing data.
(a)
(b)
(c)

## Slide 13
04
仿真结果
钻井液流变特性曲面构建：
基于二次拟合，Bingham-Papanastasiou Surface Model
Fitting of (a) plastic viscosity (R2=0.9796) and (b) yield stress (R2=0.877) as a function of temperature with data from Table 2 for the Bingham-Papanastasiou; (c) building of rheological surface models based on the Bingham-Papanastasioumodels in comparison with the testing data.
(a)
(b)
(c)

## Slide 14
02
仿真结果
钻井液流变特性曲面构建：
基于直接拟合，The Xiao Surface Model
(a) Fitting of 180 laboratory testing data to form the Xiao rheological surface (R2=0.9989) and (b) forecast of shear stress using specific shear rate and temperature through three rheological surface models in comparison with laboratory testing data listed in Table 1: assessment of relative prediction errors
(a)
(b)

## Slide 15
02
仿真结果
钻井液流变特性曲面构建：
基于直接拟合，The Xiao Surface Model
(a) Fitting of 180 laboratory testing data to form the Xiao rheological surface (R2=0.9989) and (b) relative errors between apparent viscosity predicted by the Xiao surface and the laboratory testing data listed in Table 2.
(a)
(b)

## Slide 16
02
仿真结果
钻井液挟岩能力数值仿真模型构建：
Two modules: Fluid flow and Particle Tracing for Fluid Flow
(a) Development of numerical model of Reelwell Drilling Method (RDM): inclination angle of 90°, (b) Simulation results of particle trajectories after 4s of well cleaning. 0°, 30°, 60° and 90° are four different inclination angles, and (c) Full-scale test for evaluating the cuttings carrying capacity of RDM (validation test).
(a)
(b)
(c)
Particle size: randomly distributed from 3 to 5 mm
Number of particles released: 88, 132, and 177 per 0.01s
Forces applied to particles (only three included): lift force , drag force and gravitational force

## Slide 17
02
仿真结果
钻井液挟岩能力评估：
统计Outflow pipe末端面的颗粒直径分布与数量，与Area for particle release区域释放的颗粒作比较
Chart: Particle diameter (mm)
| 3.0998 | 3.2994 | 3.4989 | 3.6984 | 3.898 | 4.0975 | 4.2971 | 4.4966 | 4.6962 | 4.8957
400 L/min | 340 | 345 | 347 | 379 | 333 | 296 | 249 | 198 | 151 | 120
(a)
(b)
(a) Cuttings carrying capacity of a certain drilling mud regarding particle size, and (b) The fraction of particles that remain at the well bottom (number of large font size, SI unit: %) labeled by size category (number of small font size, SI unit: mm).
Here, the circulation flow rate is 400L/min, inclination angle is 0°, and drilling mud temperature is 25℃.

## Slide 18
02
仿真结果
钻井液挟岩能力评估：循环流量（Circulation flow rate）的影响 （drilling mud temperature: 25℃）
Chart: Particle diameter (mm)
| 3.1 | 3.3 | 3.5 | 3.7 | 3.9 | 4.1 | 4.3 | 4.4999 | 4.6999 | 4.8999
400L/min@88 | 0.38254 | 0.38816 | 0.39041 | 0.42642 | 0.37466 | 0.33303 | 0.28015 | 0.22277 | 0.16989 | 0.13501
600L/min@88 | 0.70995 | 0.68632 | 0.66494 | 0.69532 | 0.67957 | 0.68632 | 0.67394 | 0.67057 | 0.65594 | 0.59743
800L/min@88 | 0.84721 | 0.81458 | 0.90347 | 0.90234 | 0.86971 | 0.89671 | 0.85509 | 0.89784 | 0.87196 | 0.89559
Chart: Particle diameter (mm)
| 3.1 | 3.3 | 3.5 | 3.7 | 3.9 | 4.1 | 4.3 | 4.4999 | 4.6999 | 4.8999
400L/min@88 | 0.41967 | 0.39829 | 0.39491 | 0.36566 | 0.34766 | 0.34428 | 0.33528 | 0.29253 | 0.29365 | 0.26328
600L/min@88 | 0.64694 | 0.64019 | 0.66494 | 0.61206 | 0.61769 | 0.62444 | 0.60306 | 0.61431 | 0.57606 | 0.64019
800L/min@88 | 0.73807 | 0.7527 | 0.68969 | 0.73695 | 0.68182 | 0.68632 | 0.69307 | 0.64019 | 0.67732 | 0.68857
Chart: Particle diameter (mm)
| 3.1 | 3.3 | 3.5 | 3.7 | 3.9 | 4.1 | 4.3 | 4.4999 | 4.6999 | 4.8999
400L/min@88 | 0.39154 | 0.4523 | 0.38591 | 0.40842 | 0.33866 | 0.34991 | 0.28353 | 0.25653 | 0.25765 | 0.27678
600L/min@88 | 0.65257 | 0.64581 | 0.60194 | 0.65032 | 0.55918 | 0.5243 | 0.48717 | 0.4883 | 0.49505 | 0.46805
800L/min@88 | 0.70432 | 0.71557 | 0.66944 | 0.69869 | 0.61094 | 0.66832 | 0.63794 | 0.65932 | 0.60194 | 0.60756
Chart: Particle diameter (mm)
| 3.1 | 3.3 | 3.5 | 3.7 | 3.9 | 4.1 | 4.3 | 4.4999 | 4.6999 | 4.8999
400L/min@88 | 0.37129 | 0.35554 | 0.32966 | 0.34203 | 0.30828 | 0.32741 | 0.32516 | 0.33303 | 0.33416 | 0.27903
600L/min@88 | 0.5333 | 0.56818 | 0.57493 | 0.58956 | 0.60419 | 0.56931 | 0.57156 | 0.61544 | 0.59068 | 0.56143
800L/min@88 | 0.69307 | 0.70995 | 0.76058 | 0.7077 | 0.7167 | 0.69419 | 0.66832 | 0.70432 | 0.67394 | 0.66269
(a) 0°
(c) 60°
(b) 30°
(d) 90°
(1) When the circulation flow rate is raised from 400 L/min to 600 L/min, the increments in averaged dimensionless cuttings carrying capacities for drilling pipes inclined at 0°, 30°, 60°, and 90° are documented as 116.6%, 80.6%, 63.8%, and 74.8%, respectively.
(2) Furthermore, augmenting the flow rate from 400 L/min to 800 L/min yields respective averaged growth magnitudes of 182.1%, 102.2%, 93.3%, and 111.5% for the same angles.
(3) The conclusions reached herein align closely with prior experimental evidence, reinforcing the notion that inclination angles ranging from 30° to 60° constitute a critical zone for the cuttings transportation performance (Tomren et al. 1986; Boyou et al. 2019; Deshmukh and Dewangan 2022).

## Slide 19
02
仿真结果
钻井液挟岩能力评估：钻井液温度的影响（drilling mud temperature: 25℃ and 70℃）
Figure caption: Impact of circulation flow rate on the Cuttings Transportation Efficiency (CTE) of drilling mud at (a) 25℃ and (b) 70℃ considering four inclination angles
Chart: Inclination angle
| 0° | 30° | 60° | 90°
400L/min | 31.3409 | 34.8977 | 34.3523 | 33.3864
600L/min | 67.875 | 63.0227 | 56.2841 | 58.3636
800L/min | 88.4205 | 70.5455 | 66.3977 | 70.6136
Chart: Inclination angle
| 0° | 30° | 60° | 90°
400L/min | 22.25 | 29.3977 | 27.4318 | 25.375
600L/min | 51.6477 | 59.2727 | 52.3523 | 55.5
800L/min | 77.8636 | 68.75 | 65.375 | 65.4886
(a)
(b)
Understandable findings
(1) CTEs at both 25°C and 70°C exhibit an ascending trend with escalating circulation flow rates, and the patterns of variation in CTEs under each specific inclination angle display a consistent similarity.
(2) At circulation flow rates of 400 L/min, 600 L/min, and 800 L/min, the average CTEs measured at 25°C exceed those at 70°C by 29.09%, 12.60 %, and 6.39 %, respectively.
Anticommon-sense findings
(1) At 25°C, the minimum CTE consistently emerges at an inclination angle of 60°, irrespective of whether the circulation flow rate is set at 600 L/min or 800 L/min; while for 70°C, the lowest CTE is recorded at 60° for a flow rate of 600 L/min, while at 800 L/min, it shifts to an inclination angle of 30°.
(2) When the circulation flow rate is 400 L/min, the associated lowest CTE is observed at an inclination angle of 0° for both temperatures.

## Slide 20
05
结论
COMSOL Multiphysics可模拟基于Reelwell Drilling Method洗井环节的岩屑运移过程，仿真结果能很好反映全尺寸试验过程发现的岩屑运移特征；
模拟结果显示钻井液岩屑运移效率随循环流量提高而大幅提升，符合工程实践规律；
仿真结果显示30°到60°倾斜角区间对应的钻井液岩屑运移效率最低，此结果与其他学者的既有试验研究结论高度吻合；
尚存在一些难题，需要进一步展开研究或与试验结果验证，如不同温度条件下岩屑运移效率最低对应的倾斜角不同，循环流量较小时0°倾斜角区对应最低运移效率。